## Slide 1: Ch. 14 Groundwater

## Slide 2: The WATER TABLE
cone of depression

## Slide 3: Water Table
Area where the zone of saturation and zone of aeration meet. (CAN CHANGE)
water table

## Slide 4: Zone of aeration
Between the water table and the surface, section of ground that holds some water.

## Slide 5: Zone of saturation
Part of ground where all pore spaces are filled with water.

## Slide 6: Capillary fringe
Zone where water rises because the water molecules are attracted to soil.

## Slide 7: Impermeable layer
Layer of rock where water cannot enter.

## Slide 8: Perched aquifer
Forms on top of an impermeable layer that lies above the water table.

## Slide 9: Spring
Small stream of water whose source is groundwater that has reached the surface.

## Slide 10: Ordinary well
Well that contains water up to the level of the water table.

## Slide 12: Artesian formation
When an aquifer dips underground between impermeable rock layers. Like a “sandwich”. Puts pressure on layers.

## Slide 13: Aquifer
Permeable layers of rock and sediment that store groundwater and supply wells

## Slide 14: Artesian well
Well dug to access the pressurized water between the impermeable rock layers. Pressure pushes water out of ground.

## Slide 15: Impermeable cap rock
Upper impermeable layer of an artesian formation. Usually shale.

## Slide 16: Hot Springs
Groundwater heats at great depths and rises through cracks and fissures.

## Slide 17: Geyser
Hot spring that intermittently shoots columns of hot water and steam into air due to pressure.

## Slide 18: Fumarole
Groundwater is released as steam from fissures in the ground (usually from fairly recent volcanic eruptions)

## Slide 19: Porosity
The % of a materials volume that is pore space. This is the EMPTY space in rock/holes in rock.

## Slide 20: Porosity
A soil of high porosity means that there is a great deal of air space between soil particles.

## Slide 21: Permeability
Rate at which water or liquids can pass through the pore spaces of rock.
In order for WATER to PASS THROUGH ROCK, the PORE SPACES must be CONNECTED!

## Slide 23: Capillary Action
Tendency of liquids to rise UP through a material, such as sediments.

## Slide 24: Infiltration
Process when water enters the ground through cracks in the rock.